## Slide 1
Dr. Anil Chhangani
Associate Professor
9821382455
Use Blue ray protector glasses

## Slide 2
Medium Access Control (MAC)
Medium access control comprises all mechanisms that regulate user access to a medium using
SDM
TDM
FDM
CDM

## Slide 3
MAC belongs to layer 2, the data link control
layer (DLC)
Layer 2 is subdivided into the
logical link control (LLC) layer 2 b
MAC layer 2 a

## Slide 4
The main task of DLC is to
establish a reliable point to point
or
point to multi-point connection between different
devices over a wired or wireless medium.

## Slide 5
● Data link layer: The main tasks of this layer include
Accessing the medium
Multiplexing of different data streams
Correction of transmission errors,
Synchronization ( i.e., detection of a data frame)

## Slide 6
The data link layer is responsible for a reliable point-to point connection between two devices
OR
A point-to-multipoint connection between one sender and several receivers.

## Slide 7: Motivation
Can we apply media access methods from fixed networks?
Example CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
  send as soon as the medium is free, listen into the medium if a collision occurs (original method in IEEE 802.3)
Problems in wireless networks
  signal strength decreases at least proportional to the square of the distance
  senders apply CS and CD, but the collisions happen at receivers

## Slide 8
Motivation for a specialized MAC
Whether it is possible to use MAC in wireless ?
Let us consider carrier sense multiple access with collision detection, (CSMA/CD) which works as follows.

## Slide 9
A sender senses the medium (a wire or coaxial cable) to see if it is free.
If it is busy, the sender waits until it is free.
If it is free, the sender starts transmitting data and continues to listen into the medium.
If the sender detects a collision while sending, it stops
at once and sends a jamming signal.

## Slide 10
CSMA/CD is not really interested in collisions at the sender, but rather in those at the receiver.
Sender is the one detecting collisions.
This is not a problem using a wire, as more or less the same signal strength can be assumed all over the wire.
If a collision occurs somewhere in the wire, everybody will notice it..

## Slide 11
In wireless networks the strength of a signal decreases proportionally to the square of the distance to the sender.
Obstacles attenuate the signal even further.
The sender may now apply carrier sense and detect an idle medium.
The sender starts sending – but a collision happens at the receiver due to a second sender.

## Slide 12
The sender detects no collision and assumes that the data has been transmitted without errors.
But a collision might actually have destroyed the data at the receiver.
Collision detection is very difficult in wireless scenarios
So, this common MAC scheme from wired network fails in a wireless scenario.

## Slide 13
Hidden and exposed terminals
Consider the scenario with three mobile phones as shown in following figure .
B
A
C

## Slide 14
The transmission range of A reaches B, but not C (the detection range does not reach C either).
The transmission range of C reaches B, but not A.
Finally, the transmission range of B reaches A and C.
A cannot detect C and vice versa.

## Slide 15
A starts sending to B, C does
not receive this transmission.
C also wants to send to B and senses the medium.
Medium appears to be free, the carrier sense fails.
C also starts sending causing a collision at B.
But A cannot detect this collision at B and continues with its transmission.
A is hidden for C and vice versa.
Hidden terminals may cause collisions

## Slide 16: Motivation – Hidden terminal problem
A sends to B, C cannot receive A
C wants to send to B, C senses a “free” medium (CS fails)
collision at B, A cannot receive the collision (CD fails)
A is “hidden” for C
B
A
C
R. Wattenhofer

## Slide 17: Motivation – Exposed terminal problem
B sends to A, C wants to send to D
C has to wait, CS signals a medium in use
since A is outside the radio range of C waiting is not necessary
C is “exposed” to B
B
A
C
D
R. Wattenhofer

## Slide 18
B sends something to A and
C wants to transmit data to some other mobile phone outside the interference ranges of A and B.
C senses the carrier and detects that the carrier is busy (B’s signal).
C postpones its transmission until it detects the medium as being idle again.
But as A is outside the interference range of C, waiting is not necessary

## Slide 19
Causing a ‘collision’ at B does not matter because the collision is too weak to propagate to A.
In this situation, C is exposed to B.
Exposed terminal causes unnecessary delay

## Slide 20: Motivation - near and far terminals
Terminals A and B send, C receives
  the signal of terminal B hides A’s signal
  C cannot receive A
This is also a severe problem for CDMA networks
precise power control
A
R. Wattenhofer
B
C

## Slide 21
Near and far terminals
Consider the situation as shown in Figure

## Slide 22
Near and far terminals
A and B are both sending with the same transmission power.
As the signal strength decreases proportionally to the square of the distance, B’s signal drowns out A’s signal.
As a result, C cannot receive A’s transmission.
In this case, terminal B would already drown out terminal A on the physical layer.
C in return would have no chance of applying a fair scheme as it would only hear B.

## Slide 23
The near/far effect is a severe problem of wireless networks using CDM.
All signals should arrive at the receiver with more or less the same strength.
Precise power control is needed to receive all senders with the same strength at a receiver.

## Slide 24: Multiple Access with Collision Avoidance (MACA)
R. Wattenhofer
Use short signaling packets for collision avoidance
  Request (or ready) to send RTS: a sender requests the right to send from a receiver with a short RTS packet before it sends a data packet
  Clear to send CTS: the receiver grants the right to send as soon as it is ready to receive
Signaling packets contain
  sender address
  receiver address
  packet size
Example: Wireless LAN (802.11) as DFWMAC

## Slide 25: MACA examples
MACA avoids the problem of hidden terminals
A and C want to send to B
A sends RTS first
C waits after receiving CTS from B
MACA avoids the problem of exposed terminals
B wants to send to A, and C to D
now C does not have to wait for it cannot receive CTS from A
A B
C
RTS
CTS
CTS
A
R. Wattenhofer
B
C
RTS
CTS
RTS
D

## Slide 26: MACA variant: DFWMAC in IEEE802.11
idle
wait for the right to send
wait for ACK
sender
receiver
RTS
time-out
⇓
RTS
CTS ➙ data
ACK
RxBusy
idle
wait for data
RTS ➙ RxBusy
RTS
⇓
CTS
data
⇓
ACK
time-out or corrupt data ➙ NAK
ACK: positive acknowledgement NAK: negative acknowledgement RxBusy: receiver busy
time-out or NAK
➙ RTS
R. Wattenhofer

## Slide 27
Multiple access with collision avoidance (MACA)
Solves hidden terminal problem
Does not need a base station,
Figure below shows scenario with hidden terminal
A & C both want to send to B
A has already started the transmission, but is hidden for C, C also starts with its transmission, thereby causing a collision at B.

## Slide 28
Multiple access with collision avoidance (MACA)
With MACA, A sends a request to send (RTS) first
B receives RTS contains names of sender and receiver, length of the future transmission
RTS is not heard by C , B sends clear to send (CTS)
CTS contains names of sender(A), receiver(B), length of the future transmission

## Slide 29
Multiple access with collision avoidance (MACA)
CTS is now heard by C
Medium reserved for A for duration of transmission
C is not allowed to send for duration indicated in CTS
Collision cannot occur at B during data transmission,
and the hidden terminal problem is solved
A RTS first
B receives RTS
RTS is not heard by C
B sends clear to send (CTS)
CTS - sender(A), receiver(B), length of future transmission

## Slide 30
MACA to solve the ‘exposed terminal’ problem
With MACA, B has to transmit an RTS first containing
the name of the receiver (A) and the sender (B)
C does not react to this message
A acknowledges using a CTS
C does not receive this CTS and concludes that A is outside the detection range

## Slide 31
MACA to solve the ‘exposed terminal’ problem
C concludes that A is outside the detection range
C can start its transmission assuming it will not cause a collision at A
The problem with exposed terminals is solved without fixed access patterns or a base station.
B sends RTS
C does not react
A sends CTS
C does not receive CTS

## Slide 32: Drawbacks of MACA
The overhead associated with RTS and CTS transmission for short and time critical data packet
MACA also assumes that the transmission links are symmetrical in both the uplink and downlink directions.
Otherwise a stronger sender, directed antennas etc. could counteract the above scheme

## Slide 33
Space Division Multiple Access (SDMA) is used for allocating a separated space to users in wireless networks.
A typical application involves assigning an optimal
base station to a mobile phone user.
The mobile phone may receive several base stations with different quality.
A MAC algorithm could decide which base station is best, taking into account which frequencies (FDM), time slots (TDM) or code (CDM).

## Slide 34
Space Division Multiple Access (SDMA) SDMA is
never used in isolation but always in combination with one or more other schemes.
Basis for the SDMA algorithm is formed by cells and sectorized antennas which constitute the infrastructure implementing SDM

## Slide 35
Frequency division multiple access (FDMA) comprises all algorithms allocating frequencies to transmission channels according to the frequency division multiplexing (FDM)
Allocation can either be fixed or dynamic
Channels can be assigned to the same frequency at all times, i.e., pure FDMA,
or change frequencies according to a certain pattern, i.e., FDMA combined with TDMA

## Slide 36
Frequency division multiple access (FDMA)
FDMA combined with TDMA is the common practice to circumvent narrowband interference at certain frequencies, known as frequency hopping.
Sender and receiver have to agree on a hopping pattern.
Hopping patterns are typically fixed, at least for a longer period.

## Slide 37
Frequency division multiple access (FDMA)
FDM is often used for simultaneous access to the medium by base station and mobile station in cellular networks.
Here the two partners typically establish a duplex channel, i.e., a channel that allows for simultaneous transmission in both directions.

## Slide 38
Frequency division multiple access (FDMA).
Here the two partners typically establish a duplex channel, i.e., a channel that allows for simultaneous transmission in both directions.
The two directions, mobile station to base station
and vice versa are now separated using different frequencies.
This scheme is then called frequency division duplex (FDD).

## Slide 39
Frequency division multiple access (FDMA).
In FDD both partners have to know the frequencies in advance.
Two frequencies are also known as uplink, i.e., from mobile station to base station or from ground control to satellite
and as downlink, i.e., from base station to mobile station or from satellite to ground control.

## Slide 40
As for example FDM and FDD, following figure shows the situation in a mobile phone network based on the GSM standard for 900 MHz
The basic frequency allocation scheme for GSM is fixed
All uplinks use the band between 890.2 and 915 MHz
All downlinks use band between 935.2 to 960 MHz

## Slide 41
The base station, shown on the right side, allocates a certain frequency for up- and downlink to establish a duplex channel with a mobile phone.

## Slide 42
Up- and downlink have a fixed relation
For a certain channel n.
If uplink frequency is fu = 890 MHz + n·0.2 MHz
the downlink frequency is fd = fu + 45 MHz
i.e., fd = 935 MHz + n·0.2 MHz

## Slide 43
The base station selects the channel
Each channel (uplink and downlink) has a bandwidth of 200 kHz.
The use of FDM for multiple access allows 124 channels per direction are available

## Slide 44
Time division multiple access (TDMA)
TDMA comprises all technologies that allocate certain time slots for communication TDM
The receiver can stay at the same frequency the whole time
Using only one frequency, and thus very simple receivers and transmitters
Listening to many channels separated in time at the same frequency is simple.

## Slide 45
Time division multiple access (TDMA)
Now synchronization between sender and receiver has to be achieved in the time domain.
This can be done by using a fixed pattern i.e., allocating a certain time slot for a channel
or by using a dynamic allocation scheme
Dynamic allocation schemes require an identification for each transmission e.g., sender address or the transmission has to be announced beforehand.
MAC addresses are quite often used as identification.

## Slide 46
This enables a receiver in a broadcast medium to recognize if it really is the intended receiver of a message.
Fixed schemes do not need an identification, but are not as flexible considering varying bandwidth requirements.
The following sections present several examples for fixed and dynamic schemes as used for wireless transmission.
Typically, those schemes can be combined with
FDMA to achieve even greater flexibility and transmission capacity.

## Slide 47
Fixed TDM
The simplest algorithm for using TDM is allocating time slots for channels in a fixed pattern.
This results in a fixed bandwidth and is the typical solution for wireless phone systems.
MAC is quite simple, as the only crucial factor is accessing the reserved time slot at the right moment.
If this synchronization is assured, each mobile station knows its turn and no interference will happen.

## Slide 48
The fixed pattern can be assigned by the base station, where competition between different mobile stations that want to access the medium is solved.
Fixed access patterns (at least fixed for some period in time) fit perfectly well for connections with a fixed bandwidth.
Furthermore, these patterns guarantee a fixed delay – one can transmit, e.g., every 10 ms as this is the standard
TDMA schemes with fixed access patterns are used for many digital mobile phone systems like IS-54, IS-136, GSM, DECT, PHS, and PACS.

## Slide 49
Figure 3.4 shows how these fixed TDM patterns are used to implement multiple access and a duplex channel between a base station and mobile station.
Assigning different slots for uplink and downlink using the same frequency is called time division duplex (TDD).

## Slide 50
The base station uses one out of 12 slots for the downlink, whereas the mobile station uses one out of 12 different slots for the uplink.
Uplink and downlink are separated in time.
Up to 12 different mobile stations can use the same frequency without interference using this scheme.
Each connection is allotted its own up- and downlink pair.

## Slide 52
MCC PT2 Question Bank
1 Explain UTMS Architecture
2 Write Note on Handover in UTMS
3 Explain GPRS architecture Reference Model
4 Explain Advantages and Disadvantage of Wireless LAN
5 Write Note on UTRAN
6 Write Note on Infrastructure and Ad-hoc wireless network
7. Write short notes on Hidden and exposed terminals.
Write short notes on Near and far terminals.
Write short notes on SDMA.
Write short notes on FDMA.
Write short notes on TDMA.
Compare SDMA ,TDMA,FDMA and CDMA.
Explain how Multiple Access with collision avoidance (MACA) solve
hidden terminals problem.
14. Explain how Multiple Access with collision avoidance (MACA) solve exposed terminals problem.
15. Explain agent discovery process.
16. Explain agent registration process.

## Slide 53
Multiple access with collision avoidance (MACA)
Solves hidden terminal problem
Does not need a base station,
Figure below shows scenario with hidden terminal
A & C both want to send to B
A has already started the transmission, but is hidden for C, C also starts with its transmission, thereby causing a collision at B.

## Slide 54
Multiple access with collision avoidance (MACA)
With MACA, A sends a request to send (RTS) first
B receives RTS contains names of sender and receiver, length of the future transmission
RTS is not heard by C , B sends clear to send (CTS)
CTS contains names of sender(A), receiver(B), length of the future transmission

## Slide 55
Multiple access with collision avoidance (MACA)
CTS is now heard by C
Medium reserved for A for duration of transmission
C is not allowed to send for duration indicated in CTS
Collision cannot occur at B during data transmission,
and the hidden terminal problem is solved
A RTS first
B receives RTS
RTS is not heard by C
B sends clear to send (CTS)
CTS - sender(A), receiver(B), length of future transmission

## Slide 56
MACA to solve the ‘exposed terminal’ problem
With MACA, B has to transmit an RTS first containing
the name of the receiver (A) and the sender (B)
C does not react to this message
A acknowledges using a CTS
C does not receive this CTS and concludes that A is outside the detection range

## Slide 57
MACA to solve the ‘exposed terminal’ problem
C concludes that A is outside the detection range
C can start its transmission assuming it will not cause a collision at A
The problem with exposed terminals is solved without fixed access patterns or a base station.
B sends RTS
C does not react
A sends CTS
C does not receive CTS

## Slide 58
The near/far effect is a severe problem of wireless networks using CDM.
All signals should arrive at the receiver with more or less the same strength.
Precise power control is needed to receive all senders with the same strength at a receiver.