## Slide 1
Frequencies for radio transmission
Radio transmission can take place using many different frequency bands.
Each frequency band exhibits certain advantages and disadvantages.
Figure below taken from the book “ Mobile communications “ by Jochen Schiller gives a rough overview of the frequency spectrum that can be used for data transmission.
The figure shows frequencies starting at 300 Hz and going up to over 300 THz.

## Slide 2
Directly coupled to the frequency is the wavelength λ via the equation:
λ = c/f,
where c ≅ 3·108 m/s (the speed of light in vacuum) and f the frequency.

## Slide 3
For traditional wired networks, frequencies of up to several hundred kHz are used for distances up to some km with twisted pair copper wires
While frequencies of several hundred MHz are used with coaxial cable (new coding schemes work with
several hundred MHz even with twisted pair copper wires over distances of some 100 m).
Fiber optics are used for frequency ranges of several hundred THz, but here one typically refers to the wavelength which is, e.g., 1500 nm, 1350 nm
etc. (infra red).

## Slide 4
Radio transmission starts at several kHz, the very low frequency (VLF) range.
These are very long waves.
Waves in the low frequency (LF) range are used by submarines, because these waves can
- penetrate water
- can follow the earth’s surface.

## Slide 5
The medium frequency (MF) and high frequency
(HF) ranges are typical for transmission of hundreds of radio stations either as:
Amplitude modulation (AM) between 520 kHz and 1605.5 kHz
Short wave (SW) between 5.9 MHz and 26.1 MHz.
Frequency modulation (FM) between 87.5 MHz and 108 MHz. country to country.

## Slide 6
Conventional analog TV is transmitted in ranges of
174–230 MHz and
470–790 MHz
using the very high frequency (VHF) and ultra high frequency (UHF) bands.

## Slide 7
For mobile phones with analog technology
450–465 MHz
Digital GSM (890–960 MHz, 1710–1880 MHz)
3G cellular systems following the UMTS standard
(1900–1980 MHz, 2020–2025 MHz, 2110–2190 MHz)
VHF and especially UHF allow for small antennas and relatively reliable connections for mobile telephony.

## Slide 8
Super high frequencies (SHF) are typically used for
directed microwave links (approx. 2–40 GHz)
fixed satellite services in the
C-band (4 and 6 GHz)
Ku-band (11 and 14 GHz)
Ka-band (19 and 29 GHz).

## Slide 9
Infra red (IR) transmission is used for directed links for e.g.to connect different buildings via laser links.
The most widespread IR technology, infra red data association (IrDA), uses wavelengths of
approximately 850–900 nm
to connect laptops, PDAs etc.

## Slide 10
Signals
Signals are the physical representation of data.
Users of a communication system can only exchange data through the transmission of signals.
Layer 1 of the ISO/OSI basic reference model is responsible for the conversion of data, i.e.,
bits, into signals and vice versa
Signals are functions of time and location.

## Slide 11
Signal parameters represent the data values.
The signals for radio transmission are periodic
signals, especially sine waves as carriers.
The general function of a sine wave is:
g(t) = At sin(2 π ft t + φt)
Signal parameters are the amplitude A, the frequency f, and the phase shift φ.

## Slide 12
Antennas
Used to couple the energy from the transmitter to the outside world and, in reverse, from the outside world to the receiver.
Antennas couple electromagnetic energy to and from space to and from a wire or coaxial cable

## Slide 13
A theoretical reference antenna is the
isotropic radiator
a point in space radiating equal power in all directions
All points with equal power are located on a sphere with the antenna as its center. The radiation pattern is symmetric in all directions

## Slide 14
Figure below taken from the book “Mobile communications “ by Jochen Schiller, shows a two dimensional cross-section of the real three-dimensional pattern.
However, such an antenna does not exist in reality. Real antennas all exhibit directive effects, i.e., the intensity of radiation is not the same in all directions from the antenna.

## Slide 15
The simplest real antenna is a thin, center-fed dipole, as shown in Figure below taken from the book “Mobile communications “ by Jochen Schiller.
The dipole consists of two collinear conductors of equal length, separated by a small feeding gap. The length of the dipole is half the wavelength λ of the signal to transmit results in a very efficient radiation of the energy.

## Slide 16
Signal propagation
Wireless communication networks also have senders and receivers of signals.
In wireless networks, the signal has no wire to determine the direction of propagation.
For wireless transmission, this predictable behavior is only valid in a vacuum, i.e., without matter between the sender and the receiver. The situation would be as in Figure below taken from the book
“Mobile communications “ by Jochen Schiller.

## Slide 17
Transmission range: Within a certain radius of the sender transmission is possible, i.e., a receiver receives the signals with an error rate low enough to be able to communicate and can also act as sender.

## Slide 18
Detection range: Within a second radius, detection of the transmission is possible, i.e., the transmitted power is large enough to differ from background noise.
However, the error rate is too high to establish communication.

## Slide 19
Interference range: Within a third even larger radius, the sender may interfere with other transmission by adding to the background noise.
A receiver will not be able to detect the signals, but the signals may disturb other signals.

## Slide 20
Path loss of radio signals
In free space radio signals propagate as light does ,i.e., they follow a straight line.
If such a straight line exists between a sender and a receiver it is called line-of-sight (LOS).
Even if no matter exists between the sender and the receiver (i.e., if there is a vacuum), the signal still experiences the free space loss.

## Slide 21
Path loss of radio signals
The received power Pr is proportional to 1/d^2 with d being the distance between sender and receiver (inverse square law). The reason for this phenomenon is quite simple.

## Slide 22
Radio waves can exhibit three fundamental propagation behaviors depending on their frequency:
● Ground wave (<2 MHz): Waves with low frequencies follow the earth’s surface and can propagate long distances. These waves are used for, e.g., submarine communication or AM radio.

## Slide 23
● Sky wave (2–30 MHz): Many international broadcasts and amateur radio use these short waves that are reflected at the ionosphere.
This way the waves can bounce back and forth between the ionosphere and the earth’s surface, travelling around the world.

## Slide 24
● Line-of-sight (>30 MHz): Mobile phone systems, satellite systems, cordless telephones etc. use even higher frequencies.
The emitted waves follow a (more or less) straight line of sight.
This enables direct communication with satellites
(no reflection at the ionosphere)
An additional consideration for ground-based communication is that the waves are bent by the atmosphere due to refraction